H801RC Instructions

- Introduction
  H801RC is a slave controller that transmits data based on Ethernet Protocol, data is input to NET1 and output from NET2. H801RC has eight output ports and drives maximum 8192 pixels, and can be connected to computer or master controller(H802TB or H80xTC).
  H801RC can drive the following chips:   
  LPD6803, LPD8806, LPD6812, LPD6813, LPD1882, LPD1889, LPD1883, LPD1886, DMX512, HDMX, APA102, P9813, LD1510, LD1512, LD1530, LD1532, UCS6909, UCS6912, UCS1903, UCS1909, UCS1912, WS2801, WS2803, WS2811, DZ2809, SM16716, TLS3001, TLS3002, TM1812, TM1809, TM1804, TM1803, TM1914, TM1926, TM1829, TM1906, INK1003, BS0825, BS0815, BS0901, LY6620, DM412, DM413, DM114, DM115, DM13C, DM134, DM135, DM136, 74HC595, 6B595, MBI6023, MBI6024, MBI5001, MBI5168, MBI5016, MBI5026, MBI5027, TB62726, TB62706, ST2221A, ST2221C, XLT5026, ZQL9712, ZQL9712HV, etc.
  Offline auxiliary software is “LED Build Software”; online auxiliary software is “LED Studio Software”.
2. Performance
(1). Eight output ports drive maximum 8192 pixels. Each port drives maximum 8192 divided by number of using ports pixels. Port number could be one, two, four, or eight.(means you can select “one slave with a line”, “two slave with a line”, “four slave with a line”, or “eight slave with a line” in LED Build Software)
(2). Working online or offline, H801RC can be connected to computer, master controller, switch or photoelectric converter.
(3). High synchronization performance, the transmission of adjacent slave controller delays within 400 ns, that is to say a cascade of 100 slave controllers delay within 40 microseconds and the image has no tearing or mosaic phenomenon.
(4). Good control affect and grayscale level is under precisely control.
(5). Far transmission distance. Signal transmitted based on standard Ethernet protocol and the nominal transmission distance is 100 meters. Both slave controller and network repeater can be used as repeater. And the transmission distance can reach to more than 25 kilometers by using photoelectric converter.
(6). The clock scanning frequency is adjustable within 100K to 50M Hz.
(7). Using grayscale and inverse gamma correction technology to make actual displaying effect more consistent with human physiological sensation.

- Operation Instruction

- . Connect the network card of computer (or master controller) to NET1 with network cable, then connect NET2 to NET1 of next slave controller.

- . For LPD6813 and P9813, H801RC can only drive 6144 pixels.

- . Crossover network cable is recommended in engineering. The connection is displayed as follows:

one side               the other side

- . When setting sculpt, you can choose “one line with a slave”, “two line with a slave”, “four line with a slave”, or “eight line with a slave”. Line number is port number.

| Port number | 1 | 2 | 4 | 8 |
| --- | --- | --- | --- | --- |
| Each port drive pixels | 4096 | 4096 | 2048 | 1024 |

When port number is 1, 2, or 4, the rest ports are backups of using ports.

- . There are two indicator lights besides the network interfaces, the upper one is green NET, which will flash when detect data from network cable, the below one is red ACT, which will flash when controller output data to lamp. The flash frequency is effected by data transmit rate.

- . When connect H801RC to computer, don’t select “obtain an IP address automatically” but select “Use the following IP address”, enter an IP address as follows, Subnet mask is 255.255.255.0, remember check “validate setting upon exit”.

- Ports definition

- Connection Diagram

Use optical fiber to prolong transmit distance

- Specifications

| Input Voltage | AC220V |
| --- | --- |
| Power Consumption | 1.5W |
| Drive pixels | 8192 |
| Weight | 1Kg |
| Working Temperature | -20C°--75C° |
| Dimension | L189 x W123 x H40 |
| Installation Hole Distance | 100mm |
| Carton Size | L205 x W168 x H69 |